TERMINFO(5)					   TERMINFO(5)


NAME
	terminfo - terminal capability data base

SYNOPSIS
	/usr/lib/terminfo

DESCRIPTION

	[This manual is incomplete, so take everything with a pinch of salt]

	Terminfo is a data base describing terminals.  It is used,
	for  example,  by  vi(1) and  curses(3).   Terminals  are
	described  in  terminfo	by  giving  a set of capabilities
	which they have and by describing how operations are  per-
	formed.	Padding requirements and initialization sequences
	are included in terminfo.

	Entries in terminfo consist of a number of comma-separated
	fields.	White	space  after  each comma is ignored.  The
	first entry for each terminal gives the	names  which  are
	known  for the terminal, separated by `|' characters.  The
	first name given is the most common abbreviation for  the
	terminal,  the last name given should be a long name fully
	identifying the terminal, and all others are understood as
	synonyms for  the  terminal name.  All names but the last
	should be in lower case and contain no  blanks;	the  last
	name  may well contain upper case and blanks for readabil-
	ity.

	Terminal names (except for the last, verbose entry) should
	be chosen using the following conventions.  The particular
	piece of hardware making up the	terminal  should  have	a
	root  name  chosen, thus ``hp2621''.  This name should not
	contain hyphens, except that synonyms may be  chosen  that
	do not conflict with other names.  Modes that the hardware
	can be in, or user preferences,	should	be  indicated  by
	appending  a hyphen and an indicator of the mode.  Thus, a
	vt100 in 132 column mode would be vt100-w.  The	following
	suffixes should be used where possible:

	Suffix	Meaning				 Example
	-w	Wide mode (more than 80 columns)	vt100-w
	-am	With auto. margins (usually default)	vt100-am
	-nam	Without automatic margins		vt100-nam
	-n	Number of lines on the screen		aaa-60
	-na	No arrow keys (leave them in local)	c100-na
	-np	Number of pages of memory		c100-4p
	-rv	Reverse video				c100-rv

CAPABILITIES
	The  variable  is the name by which the programmer (at the
	terminfo level) accesses the capability. The  capname  is
	the  short  name used in the text of the database, and is
	used by a person updating the database.

	Capability names have no hard length limit, but an  infor-
	mal  limit  of  5 characters has been adopted to keep them
	short.  Whenever possible, names are chosen to be the same
	as  or similar to the ANSI X3.64-1979 standard.	Semantics
	are also intended to match those of the specification.

	(P)	indicates padding may be specified
	(G)	indicates that the string is passed through tparm with
		 parms as given (#i).
	(*)	indicates that padding may be based on the number of
		 lines affected
	(#i)	indicates the ith parameter.

----------------------------------------------------------------------------------------------------
	List of Capabilities:

term.h name		     terminfo	 termcap   description

	Boolean capabilities:
	---------------------

auto_left_margin	 	"bw"		"bw"	cub1 wraps from column 0 to last column
auto_right_margin		"am"		"am"	terminal has automatic margins
no_esc_ctlc	      		"xsb"		"xb"	beehive (f1=escape, f2=ctrl C)
ceol_standout_glitch    	"xhp"		"xs"	stnadout not erased by overwriting (hp)
eat_newline_glitch      	"xenl"		"xn"	newline ignored after 80 cols (concept)
erase_overstrike	 	"eo"		"eo"	can erase overstrikes with a blank
generic_type	     		"gn"		"gn"	generic line type
hard_copy	        	"hc"		"hc"	hardcopy terminal
has_meta_key	     		"km"		"km"	Has a meta key, sets msb high
has_status_line	  		"hs"		"hs"	has extra status line
insert_null_glitch      	"in"		"in"	insert mode distinguishes nulls
memory_above	     		"da"		"da"	display may be retained above the screen
memory_below	     		"db"		"db"	display may be retained below the screen
move_insert_mode	 	"mir"		"mi"	safe to move while in insert mode
move_standout_mode      	"msgr"		"ms"	safe to move while in standout mode
over_strike	      		"os"		"os"	terminal can overstrike
status_line_esc_ok      	"eslok"		"es"	escape can be used on the status line
dest_tabs_magic_smso    	"xt"		"xt"	tabs destructive, magic so char (t1061)
tilde_glitch	     		"hz"		"hz"	can't print ~'s (hazeltine)
transparent_underline   	"ul"		"ul"	underline character overstrikes
xon_xoff	         	"xon"		"xo"	terminal uses xon/xoff handshaking
needs_xon_xoff	   		"nxon"		"nx"	padding won't work, xon/xoff required
prtr_silent	      		"mc5i"		"5i"	printer won't echo on screen
hard_cursor	      		"chts"		"HC"	cursor is hard to see
non_rev_rmcup	    		"nrrmc"		"NR"	smcup does not revrse rmcup
no_pad_char	      		"npc"		"NP"	pad character does not exist
non_dest_scroll_region  	"ndscr"		"ND"	scrolling region is non-destructive
back_color_erase	 	"bce"		"ut"	screen erased with background color
can_change	       		"ccc"		"cc"	terminal can re-define exiting colors
col_addr_glitch	  		"xhpa"		"YA"	only positive motion for hpa/mhpa caps
cpi_changes_res	  		"cpix"		"YF"	changing character pitch changes resolution
cr_cancels_micro_mode   	"crxm"		"YB"	using cr turns off micro mode
has_print_wheel	  		"daisy"		"YC"	printer needs operator to change character set
hue_lightness_saturation	"hls"		"hl"	terminal uses only HLS color notation (tektronix)
lpi_changes_res	  		"lpix"		"YG"	chnaging line pitch changes resolution
row_addr_glitch	  		"xvpa"		"YD"	only posistive motion for vhp/mvpa caps
semi_auto_right_margin  	"sam"		"YE"	printing in last column causes cr

	Numerical capabilities:
	-----------------------

columns	          		"cols"		"co"	number of columns in aline
init_tabs	        	"it"		"it"	tabs initially every # spaces
lines	            		"lines"		"li"	number of lines on screen or page
lines_of_memory	  		"lm"		"lm"	lines of memory if > line. 0 => varies
magic_cookie_glitch     	"xmc"		"sg"	number of blank chars left by smso or rmso
padding_baud_rate		"pb"		"pb"	lowest baud rate where padding needed
virtual_terminal	 	"vt"		"vt"	virtual terminal number (CB/unix)
width_status_line		"wsl"		"ws"	columns in status line
num_labels	       		"nlab"	   	"Nl"	number of lables on screen
label_height	     		"lh"		"lh"	rows in each label
label_width	      		"lw"		"lw"	columns in each label
max_attributes	   		"ma"		"ma"	maximum combined attributes terminal can handle
maximum_windows	  		"wnum"	   	"MW"	maxumum number of defineable windows
bit_image_entwining    		"bitwin"	"Yo"	??
bit_image_type	   		"bitype"	"Yp"	??
buffer_capacity	  		"bufsz"		"Ya"	numbers of bytes buffered before printing
buttons	          		"btns"		"BT"	??
dot_horz_spacing	 	"spinh"		"Yc"	spacing of pins vertically in pins per inch
dot_vert_spacing	 	"spinv"		"Yb"	spacing of dots horizontally in dots per inch
max_colors	       		"colors"	"Co"	maximum numbers of colors on screen
max_micro_address		"maddr"		"Yd"	maximum value in micro_..._address
max_micro_jump	   		"mjump"		"Ye"	maximum value in parm_..._micro
max_pairs	        	"pairs"		"pa"	maximum number of color-pairs on the screen
micro_char_size	  		"mcs"		"Yf"	??
micro_line_size	  		"mls"		"Yg"	??
no_color_video	   		"ncv"		"NC"	video attributes that can't be used with colors
number_of_pins	   		"npins"	   	"Yh"	numbers of pins in print-head
output_res_char	  		"orc"		"Yi"	horizontal resolution in units per line
output_res_horz_inch   		"orhi"		"Yk"	horizontal resolution in units per inch
output_res_line	  		"orl"		"Yj"	vertical resolution in units per line
output_res_vert_inch    	"orvi"		"Yl"	vertical resolution in units per inch
print_rate	       		"cps"		"Ym"	print rate in chars per second
wide_char_size	   		"widcs"		"Yn"	character step size when in double wide mode

	String capabilites:
	-------------------

back_tab	         	"cbt"		"bt"	back tab
bell	             		"bel"		"bl"	audible signal (bell)
carriage_return	  		"cr"		"cr"	carriage return
change_scroll_region    	"csr"		"cs"	change region to line #1 to line #2
clear_all_tabs	   		"tbc"		"ct"	clear all tab stops
clear_screen	     		"clear"		"cl"	clear screen and home cursor
clr_eol	          		"el"		"ce"	clear to end of line
clr_eos	          		"ed"		"cd"	clear to edn of screen
column_address	   		"hpa"		"ch"	horizontal position, absolute
command_character		"cmdch"		"CC"	terminal settable cmd character in prototype !?
cursor_address	   		"cup"		"cm"	move to row #1 columns #2
cursor_down	      		"cud1"		"do"	down one line
cursor_home	      		"home"		"ho"	home cursor (if no cup)
cursor_invisible	 	"civis"		"vi"	make cursor invisible
cursor_left	      		"cub1"		"le"	move left one space
cursor_mem_address      	"mrcup"		"CM"	memory relative cursor addressing
cursor_normal	    		"cnorm"		"ve"	make cursor appear normal (undo civis/cvvis)
cursor_right	     		"cuf1"		"nd"	move right one space
cursor_to_ll	     		"ll"		"ll"	last line, first column (if no cup)
cursor_up	        	"cuu1"		"up"	up one line
cursor_visible	   		"cvvis"		"vs"	make cursor very visible
delete_character	 	"dch1"		"dc"	delete character
delete_line	      		"dl1"		"dl"	delete line
dis_status_line	  		"dsl"		"ds"	disable status line
down_half_line	   		"hd"		"hd"	half a line down
enter_alt_charset_mode  	"smacs"		"as"	start alternate character set
enter_blink_mode	 	"blink"		"mb"	turn on blinking
enter_bold_mode	  		"bold"		"md"	turn on bold (extra bright) mode
enter_ca_mode	    		"smcup"		"ti"	string to start programs using cup
enter_delete_mode		"smdc"		"dm"	enter delete mode
enter_dim_mode	   		"dim"		"mh"	turn on half-bright mode
enter_insert_mode		"smir"		"im"	enter insert mode
enter_secure_mode		"invis"		"mk"	turn on blank mode (characters invisible)
enter_protected_mode    	"prot"		"mp"	turn on protected mode
enter_reverse_mode      	"rev"		"mr"	turn on reverse video mode
enter_standout_mode     	"smso"		"so"	begin standout mode
enter_underline_mode    	"smul"		"us"	begin underline mode
erase_chars	      		"ech"		"ec"	erase #1 characters
exit_alt_charset_mode   	"rmacs"		"ae"	end alternate character set
exit_attribute_mode     	"sgr0"		"me"	turn off all attributes
exit_ca_mode	     		"rmcup"		"te"	strings to end programs using cup
exit_delete_mode	 	"rmdc"		"ed"	end delete mode
exit_insert_mode	 	"rmir"		"ei"	exit inset mode
exit_standout_mode      	"rmso"		"se"	exit standout mode
exit_underline_mode     	"rmul"		"ue"	exit underline mode
flash_screen	     		"flash"		"vb"	visible bell (may not move cursor)
form_feed	        	"ff"		"ff"	hardcopy terminal page eject
from_status_line	 	"fsl"		"fs"	return from status line
init_1string	     		"is1"	   	"i1"	initialization string
init_2string	     		"is2"	   	"is"	initialization string
init_3string	     		"is3"	   	"i3"	initialization string
init_file	        	"if"		"if"	name of initialization file
insert_character	 	"ich1"		"ic"	insert character
insert_line	      		"il1"		"al"	insert line
insert_padding	   		"ip"		"ip"	insert padding after inserted character
key_backspace	    		"kbs"		"kb"	backspace key
key_catab	        	"ktbc"		"ka"	clear-all-tabs key
key_clear	        	"kclr"		"kC"	clear-screen or erase key
key_ctab	         	"kctab"		"kt"	clear-tab key
key_dc	           		"kdch1"		"kD"	delete-character key
key_dl	           		"kdl1"		"kL"	delete-line key
key_down	         	"kcud1"		"kd"	down-arrow key
key_eic	          		"krmir"		"kM"	sent by rmir or smir in insert mode
key_eol	          		"kel"		"kE"	clear-to-end-of-line key
key_eos	          		"ked"		"kS"	clear-to-end-of-screen key
key_f0	           		"kf0"		"k0"	F0 function key
key_f1	           		"kf1"		"k1"	F1 function key
key_f10	          		"kf10"		"k;"	F10 function key
key_f2				"kf2"   	"k2"	F2 function key
key_f3				"kf3"   	"k3"	F3 function key
key_f4				"kf4"   	"k4"	F4 function key
key_f5				"kf5"   	"k5"	F5 function key
key_f6				"kf6"   	"k6"	F6 function key
key_f7	           		"kf7"		"k7"	F7 function key
key_f8	           		"kf8"		"k8"	F8 fucntion key
key_f9	           		"kf9"		"k9"	F9 function key
key_home	         	"khome"		"kh"	home key
key_ic	           		"kich1"		"kI"	insert-character key
key_il	           		"kil1"		"kA"	insert-line key
key_left	         	"kcub1"		"kl"	left-arrow key
key_ll	           		"kll"		"kH"	last-line key
key_npage	        	"knp"		"kN"	next-page key
key_ppage	        	"kpp"		"kP"	prev-page key
key_right	        	"kcuf1"		"kr"	right-arrow key
key_sf	           		"kind"		"kF"	scroll-forward key
key_sr	           		"kri"		"kR"	scroll-backward key
key_stab	         	"khts"		"kT"	set-tab key
key_up	           		"kcuu1"		"ku"	up-arrow key
keypad_local	     		"rmkx"		"ke"	out of 'keyoad_transmit' mode
keypad_xmit	      		"smkx"		"ks"	enter into 'keyboard_transmit' mode
lab_f0	           		"lf0"		"l0"	label on function key f0 if not f0
lab_f1	           		"lf1"		"l1"	label on function key f1 if not f1
lab_f10	          		"lf10"		"la"	label on function key f10 if not f10
lab_f2	           		"lf2"		"l2"	label on function key f2 if not f2
lab_f3	           		"lf3"		"l3"	label on function key f3 if not f3
lab_f4	           		"lf4"		"l4"	label on function key f4 if not f4
lab_f5	           		"lf5"		"l5"	lable on function key f5 if not f5
lab_f6	           		"lf6"		"l6"	label on function key f6 if not f6
lab_f7	           		"lf7"		"l7"	label on function key f7 if not f7
lab_f8	           		"lf8"		"l8"	label on function key f8 if not f8
lab_f9	           		"lf9"		"l9"	label on function key f9 if not f9
meta_off	         	"rmm"		"mo"	turn off meta mode
meta_on	          		"smm"		"mm"	turn on meta mode (8th-bit on)
newline	          		"nel"		"nw"	newline (behave like cr followed be lf)
pad_char	         	"pad"		"pc"	padding char (instead of null)
parm_dch	         	"dch"		"DC"	delete #1 chars
parm_delete_line	 	"dl"		"DL"	delete #1 lines
parm_down_cursor	 	"cud"		"DO"	down #1 lines
parm_ich	         	"ich"		"IC"	insert #1 chars
parm_index	       		"indn"		"SF"	scroll forward #1 lines
parm_insert_line	 	"il"		"AL"	insert #1 lines
parm_left_cursor	 	"cub"		"LE"	move #1 chars to the left
parm_right_cursor		"cuf"		"RI"	move #1 chars to the right
parm_rindex	      		"rin"		"SR"	scroll back #1 lines
parm_up_cursor	   		"cuu"		"UP"	up #1 lines
pkey_key	       	 	"pfkey"		"pk"	program function key #1 to type string #2
pkey_local	       		"pfloc"		"pl"	program function key #1 to execute string #2
pkey_xmit	        	"pfx"		"px"	program function key #1 to transmit string #2
print_screen	     		"mc0"		"ps"	print contents of screen
prtr_off	         	"mc4"		"pf"	turn off printer
prtr_on	          		"mc5"		"po"	turn on printer
repeat_char	      		"rep"		"rp"	repeat char #1 #2 times
reset_1string	    		"rs1"	   	"r1"	reset string
reset_2string	    		"rs2"	   	"r2"	reset string
reset_3string	    		"rs3"	   	"r3"	reset string
reset_file	       		"rf"		"rf"	name of reset file
restore_cursor	   		"rc"		"rc"	restore cursor to last position of sc
row_address	      		"vpa"		"cv"	vertical position absolute
save_cursor	      		"sc"		"sc"	save current cursor position
scroll_forward	   		"ind"		"sf"	scroll text up
scroll_reverse	   		"ri"		"sr"	scroll text down
set_attributes	   		"sgr"		"sa"	define video attributes #1-#9
set_tab	          		"hts"		"st"	set a tab in every row, current columns
set_window	       		"wind"		"wi"	current window is lines #1-#2 cols #3-#4
tab	              		"ht"		"ta"	tab to next 8-space hardware tab stop
to_status_line	   		"tsl"		"ts"	move to status line
underline_char	   		"uc"		"uc"	underline char and move past it
up_half_line	     		"hu"		"hu"	half a line up
init_prog	        	"iprog"		"iP"	path name of program for initialization
key_a1	           		"ka1"		"K1"	upper left of keypad
key_a3	           		"ka3"		"K3"	upper right of keypad
key_b2	           		"kb2"		"K2"	center of keypad
key_c1	           		"kc1"		"K4"	lower left of keypad
key_c3	           		"kc3"		"K5"	lower right of keypad
prtr_non	         	"mc5p"		"pO"	turn on printer for #1 bytes
char_padding	     		"rmp"		"rP"	like ip but when in insert mode
acs_chars	        	"acsc"		"ac"	graphics charset pairs - def=vt100
plab_norm	        	"pln"		"pn"	program label #1 to show string #2
key_btab	         	"kcbt"		"kB"	back-tab key
enter_xon_mode	   		"smxon"		"SX"	turn on xon/xoff handshaking
exit_xon_mode	    		"rmxon"		"RX"	turn off xon/xoff handshaking
enter_am_mode	    		"smam"		"SA"	turn on automatic margins
exit_am_mode	     		"rmam"		"RA"	turn off automatic margins
xoff_character	   		"xoffc"		"XF"	XON character
xon_character	    		"xonc"		"XN"	XOFF character
ena_acs	          		"enacs"		"eA"	enable alternate char set
label_on	         	"smln"		"LO"	turn on soft labels
label_off	        	"rmln"		"LF"	turn off soft labels
key_beg	          		"kbeg"		"@1"	begin key
key_cancel	       		"kcan"		"@2"	cancel key
key_close	        	"kclo"		"@3"	close key
key_command	      		"kcmd"		"@4"	command key
key_copy	         	"kcpy"		"@5"	copy key
key_create	       		"kcrt"		"@6"	create key
key_end	          		"kend"		"@7"	end key
key_enter	        	"kent"		"@8"	enter/send key
key_exit	         	"kext"		"@9"	exit key
key_find	         	"kfnd"		"@0"	find key
key_help	         	"khlp"		"%1"	help key
key_mark	         	"kmrk"		"%2"	mark key
key_message	      		"kmsg"		"%3"	message key
key_move	         	"kmov"		"%4"	move key
key_next	         	"knxt"		"%5"	next key
key_open	         	"kopn"		"%6"	open key
key_options	      		"kopt"		"%7"	options key
key_previous	     		"kprv"		"%8"	previous key
key_print	        	"kprt"		"%9"	print key
key_redo	         	"krdo"		"%0"	redo key
key_reference	    		"kref"		"&1"	reference key
key_refresh	      		"krfr"		"&2"	refresh key
key_replace	      		"krpl"		"&3"	replace key
key_restart	      		"krst"		"&4"	restart key
key_resume	       		"kres"		"&5"	resume key
key_save	         	"ksav"		"&6"	save key
key_suspend	      		"kspd"		"&7"	suspend key
key_undo	         	"kund"		"&8"	undo key
key_sbeg	         	"kBEG"		"&9"	shifted begin key
key_scancel	      		"kCAN"		"&0"	shifted cancel key
key_scommand	     		"kCMD"		"*1"	shifted command key
key_scopy	        	"kCPY"		"*2"	shifted copy key
key_screate	      		"kCRT"		"*3"	shifted create key
key_sdc	          		"kDC"		"*4"	shifted delete char key
key_sdl	          		"kDL"		"*5"	shifted delete line key
key_select	       		"kslt"		"*6"	select key
key_send	         	"kEND"		"*7"	shifted end key
key_seol	         	"kEOL"		"*8"	shifted end of line key
key_sexit	        	"kEXT"		"*9"	shifted exit key
key_sfind	        	"kFND"		"*0"	shifted find key
key_shelp	        	"kHLP"		"#1"	shifted help key
key_shome	        	"kHOM"		"#2"	shifted home key
key_sic	          		"kIC"		"#3"	shifted insert char key
key_sleft	        	"kLFT"		"#4"	shifted left key
key_smessage	     		"kMSG"		"%a"	shifted message key
key_smove	        	"kMOV"		"%b"	shifted move key
key_snext	        	"kNXT"		"%c"	shifted next key
key_soptions	     		"kOPT"		"%d"	shifted options key
key_sprevious	    		"kPRV"		"%e"	shifted previous key
key_sprint	       		"kPRT"		"%f"	shifted print key
key_sredo	       		"kRDO"		"%g"	shifted redo key
key_sreplace	     		"kRPL"		"%h"	shifted replace key
key_sright	       		"kRIT"		"%i"	shifted right key
key_srsume	       		"kRES"		"%j"	shifted resume key
key_ssave	        	"kSAV"		"!1"	shifted save key
key_ssuspend	     		"kSPD"		"!2"	shifted suspend key
key_sundo	        	"kUND"		"!3"	shifted undo key
req_for_input	    		"rfi"		"RF"	request for input
key_f11	          		"kf11"		"F1"	F11 function key
key_f12	          		"kf12"		"F2"	F12 function key
key_f13	          		"kf13"		"F3"	F13 function key
key_f14	          		"kf14"		"F4"	F14 function key
key_f15	          		"kf15"		"F5"	F15 function key
key_f16	          		"kf16"		"F6"	F16 function key
key_f17	          		"kf17"		"F7"	F17 function key
key_f18	          		"kf18"		"F8"	F18 function key
key_f19	          		"kf19"		"F9"	F19 function key
key_f20	          		"kf20"		"FA"	F20 function key
key_f21	          		"kf21"		"FB"	F21 function key
key_f22	          		"kf22"		"FC"	F22 function key
key_f23	          		"kf23"		"FD"	F23 function key
key_f24	          		"kf24"		"FE"	F24 function key
key_f25	          		"kf25"		"FF"	F25 function key
key_f26	          		"kf26"		"FG"	F26 function key
key_f27	          		"kf27"		"FH"	F27 function key
key_f28	          		"kf28"		"FI"	F28 function key
key_f29	          		"kf29"		"FJ"	F29 function key
key_f30	          		"kf30"		"FK"	F30 function key
key_f31	          		"kf31"		"FL"	F31 function key
key_f32	          		"kf32"		"FM"	F32 function key
key_f33	          		"kf33"		"FN"	F33 function key
key_f34	          		"kf34"		"FO"	F34 function key
key_f35	          		"kf35"		"FP"	F35 function key
key_f36	          		"kf36"		"FQ"	F36 function key
key_f37	          		"kf37"		"FR"	F37 function key
key_f38	          		"kf38"		"FS"	F38 function key
key_f39	          		"kf39"		"FT"	F39 function key
key_f40	          		"kf40"		"FU"	F40 function key
key_f41	          		"kf41"		"FV"	F41 function key
key_f42	          		"kf42"		"FW"	F42 function key
key_f43	          		"kf43"		"FX"	F43 function key
key_f44	          		"kf44"		"FY"	F44 function key
key_f45	          		"kf45"		"FZ"	F45 function key
key_f46	          		"kf46"		"Fa"	F46 function key
key_f47	          		"kf47"		"Fb"	F47 function key
key_f48	          		"kf48"		"Fc"	F48 function key
key_f49	          		"kf49"		"Fd"	F49 function key
key_f50	          		"kf50"		"Fe"	F50 function key
key_f51	          		"kf51"		"Ff"	F51 function key
key_f52	          		"kf52"		"Fg"	F52 function key
key_f53	          		"kf53"		"Fh"	F53 function key
key_f54	          		"kf54"		"Fi"	F54 function key
key_f55	          		"kf55"		"Fj"	F55 function key
key_f56	          		"kf56"		"Fk"	F56 function key
key_f57	          		"kf57"		"Fl"	F57 function key
key_f58	          		"kf58"		"Fm"	F58 function key
key_f59	          		"kf59"		"Fn"	F59 function key
key_f60	          		"kf60"		"Fo"	F60 function key
key_f61	          		"kf61"		"Fp"	F61 function key
key_f62	          		"kf62"		"Fq"	F62 function key
key_f63	          		"kf63"		"Fr"	F63 function key
clr_bol	          		"el1"		"cb"	Clear to beginning of line
clear_margins	    		"mgc"		"MC"
set_left_margin	  		"smgl"		"ML"
set_right_margin	 	"smgr"		"MR"
label_format	     		"fln"		"Lf"
set_clock	        	"sclk"		"SC"
display_clock	    		"dclk"		"DK"
remove_clock	     		"rmclk"		"RC"
create_window	    		"cwin"		"CW"
goto_window	      		"wingo"		"WG"
hangup	           		"hup"		"HU"
dial_phone	       		"dial"		"DI"
quick_dial	       		"qdial"		"QD"
tone	             		"tone"		"TO"
pulse	            		"pulse"		"PU"
flash_hook	       		"hook"		"fh"
fixed_pause	      		"pause"		"PA"
wait_tone	        	"wait"		"WA"
user0	            		"u0"		"u0"	User string # 0
user1	            		"u1"		"u1"	User string # 1
user2	            		"u2"		"u2"	User string # 2
user3	            		"u3"		"u3"	User string # 3
user4	            		"u4"		"u4"	User string # 4
user5	            		"u5"		"u5"	User string # 5
user6	            		"u6"		"u6"	User string # 6
user7	            		"u7"		"u7"	User string # 7
user8	            		"u8"		"u8"	User string # 8
user9	            		"u9"		"u9"	User string # 9
# These are newer capabilities, order is random until I know better
alt_scancode_esc	 	"scesa"		"S8"
bit_image_carriage_return	"bicr"		"Yv"
bit_image_newline		"binel"		"Zz"
bit_image_repeat	 	"birep"		"Xy"
change_char_pitch		"cpi"		"ZA"
change_line_pitch		"lpi"		"ZB"
change_res_horz	  		"chr"		"ZC"
change_res_vert	  		"cvr"		"ZD"
char_set_names	   		"csnm"		"Zy"
code_set_init	    		"csin"		"ci"
color_names	      		"colornm"	"Yw"
define_bit_image_region 	"defbi"		"Yx"
define_char	      		"defc"		"ZE"
device_type	      		"devt"		"dv"
display_pc_char	  		"dispc"		"S1"
end_bit_image_region    	"endbi"		"Yy"
enter_doublewide_mode   	"swidm"		"ZF"
enter_draft_quality     	"sdrfq"		"ZG"
enter_italics_mode      	"sitm"		"ZH"
enter_leftward_mode     	"slm"		"ZI"
enter_micro_mode	 	"smicm"		"ZJ"
enter_near_letter_quality	"snlq"		"ZK"
enter_normal_quality    	"snrmq"		"ZL"
enter_pc_charset_mode   	"smpch"		"S2"
enter_scancode_mode     	"smsc"		"S4"
enter_shadow_mode		"sshm"		"ZM"
enter_subscript_mode    	"ssubm"		"ZN"
enter_superscript_mode  	"ssupm"		"ZO"
enter_upward_mode		"sum"		"ZP"
exit_doublewide_mode    	"rwidm"		"ZQ"
exit_italics_mode		"ritm"		"ZR"
exit_leftward_mode      	"rlm"		"ZS"
exit_micro_mode	  		"rmicm"		"ZT"
exit_pc_charset_mode    	"rmpch"		"S3"
exit_scancode_mode      	"rmsc"		"S5"
exit_shadow_mode	 	"rshm"		"ZU"
exit_subscript_mode     	"rsubm"		"ZV"
exit_superscript_mode   	"rsupm"		"ZW"
exit_upward_mode	 	"rum"		"ZX"
get_mouse	        	"getm"		"Gm"
initialize_color	 	"initc"		"Ic"
initialize_pair	  		"initp"		"Ip"
key_mouse	        	"kmous"		"Km"
micro_column_address    	"mhpa"		"ZY"
micro_down	       		"mcud1"		"ZZ"
micro_left	       		"mcub1"		"Za"
micro_right	      		"mcuf1"		"Zb"
micro_row_address		"mvpa"		"Zc"
micro_up	         	"mcuu1"		"Zd"
mouse_info	       		"minfo"		"Mi"
order_of_pins	    		"porder"	"Ze"
orig_colors	      		"oc"		"oc"
orig_pair	       		"op"		"op"
parm_down_micro	  		"mcud"		"Zf"
parm_left_micro	  		"mcub"		"Zg"
parm_right_micro	 	"mcuf"		"Zh"
parm_up_micro	    		"mcuu"		"Zi"
pc_term_options	  		"pctrm"		"S6"
pkey_plab	        	"pfxl"		"xl"
req_mouse_pos	    		"reqmp"		"RQ"
scancode_escape	  		"scesc"		"S7"
select_char_set	  		"scs"		"Zj"
set0_des_seq	     		"s0ds"		"s0"
set1_des_seq	     		"s1ds"		"s1"
set2_des_seq	     		"s2ds"		"s2"
set3_des_seq	     		"s3ds"		"s3"
set_a_background	 	"setab"		"AB"
set_a_foreground	 	"setaf"		"AF"
set_background	   		"setb"		"Sb"
set_bottom_margin		"smgb"		"Zk"
set_bottom_margin_parm  	"smgbp"		"Zl"
set_color_band	   		"setcolor"	"Yz"
set_color_pair	   		"scp"		"sp"
set_foreground	   		"setf"		"Sf"
set_lr_margin	    		"smglr"		"ML"
set_page_length	  		"slines"	"YZ"
set_left_margin_parm    	"smglp"		"Zm"
set_right_margin_parm   	"smgrp"		"Zn"
set_tb_margin	    		"smgtb"		"MT"
set_top_margin	   		"smgt"		"Zo"
set_top_margin_parm     	"smgtp"		"Zp"
start_bit_image	  		"sbim"		"Zq"
start_char_set_def      	"scsd"		"Zr"
stop_bit_image	   		"rbim"		"Zs"
stop_char_set_def		"rcsd"		"Zt"
subscript_characters    	"subcs"		"Zu"
superscript_characters  	"supcs"		"Zv"
these_cause_cr	   		"docr"		"Zw"
zero_motion	      		"zerom"		"Zx"
backspace_if_not_bs     	"OTbc"		"bc"
other_non_function_keys 	"OTko"		"ko"
arrow_key_map	    		"OTma"		"ma"
memory_lock_above		"OTml"		"ml"
memory_unlock	    		"OTmu"		"mu"
linefeed_if_not_lf      	"OTnl"		"nl"
key_interrupt_char      	"UWki"		"ki"
key_kill_char	    		"UWkk"		"kk"
key_suspend_char	 	"UWkz"		"kz"
scroll_left	      		"sl1"		"Sl"
scroll_right	     		"sr1"		"Sr"
parm_scroll_left	 	"sl"		"SL"
parm_scroll_right		"sr"		"SR"
------------------------------------------------------------------------------------------------------------

	A Sample Entry
	--------------
	The following entry, which describes the Concept-100,  is
	among  the more complex entries in the terminfo file as of
	this writing.

	concept100|c100|concept|c104|c100-4p|concept 100,
	  is2=\EU\Ef\E7\E5\E8\El\ENH\EK\E\200\Eo&\200\Eo\47\E,
	  cr=^M, cud1=^J, ind=^J, bel=^G, smcup=\EU\Ev	8p\Ep\r,
	  rmcup=\Ev    $<6>\Ep\r\n, il1=\E^R$<3*>, am, cub1=^H,
	  ed=\E^C$<16*>, el=\E^U$<16>, clear=^L$<2*>,
	  cup=\Ea%p1%' '%+%c%p2%' '%+%c, cols#80, dch1=\E^A$<16*>,
	  dl1=\E^B$<3*>, rmir=\E\200, eo, smir=\E^P, in, ip=$<16*>,
	  lines#24, mir, cuf1=\E=, ht=\t$<8>, kbs=^h, ul, cuu1=\E;,
	  db, smul=\EG, rmul=\Eg, xenl, cvvis=\EW, cnorm=\Ew,
	  flash=\Ek$<20>\EK, pb#9600, vt#8, smul=\EG, rmul=\Eg,
	  smso=\EE\ED, rmso=\Ed\Ee, dim=\EE, rev=\ED, blink=\EC,
	  prot=\EI, invis=\EH, sgr0=\EN\200, rep=\Er%p1%c%p2%' '%+%c$<.2*>,
	  smkx=\EX, rmkx=\Ex, kcuu1=\E;, kcud1=\E<, kcub1=\E>,
	  kcuf1=\E=, khome=\E?, kf1=\E5, kf2=\E6, kf3=\E7,

	Entries may continue onto multiple lines by placing  white
	space  at  the  beginning  of  each line except the first.
	Comments may be included on lines  beginning  with  ``#''.
	Capabilities in terminfo are of three types: Boolean capa-
	bilities which indicate that the terminal has some partic-
	ular  feature, numeric capabilities giving the size of the
	terminal or the size  of particular  delays,  and  string
	capabilities,  which  give a sequence which can be used to
	perform particular terminal operations.

	Types of Capabilities

	All capabilities have short codes.  For instance, the fact
	that  the Concept has automatic margins (i.e. an automatic
	return and linefeed when the end of a line is reached)  is
	indicated  by the capability am. Hence the description of
	the Concept includes am. Numeric  capabilities	are  fol-
	lowed  by the character `#' and then the value.	Thus cols
	which indicates the number of  columns  the  terminal  has
	gives the value `80' for the Concept.

	Finally, string valued capabilities, such as el (clear to
	end of line sequence) are given by the two character code,
	an  `=', and  then  a string ending at the next following
	`,'.  A delay in milliseconds may appear anywhere in  such
	a   capability,	enclosed   in	$<..>	brackets,  as  in
	el=\EK$<3>, and padding characters are supplied	by  tputs
	to  provide this delay.	The delay can be either a number,
	e.g. `20', or a number followed by an `*', i.e.	`3*'.	A
	`*' indicates that the padding required is proportional to
	the number of lines affected by	the  operation,	and  the
	amount  given  is  the per-affected-unit padding required.
	(In the case of insert character, the factor is still  the
	number  of  lines affected.  This is always one unless the
	terminal has xenl and the software uses it.)  When  a  `*'
	is  specified,  it  is sometimes useful to give a delay of
	the form `3.5' to specify a delay per unit  to  tenths  of
	milliseconds.  (Only one decimal place is allowed.)

	A  number  of  escape sequences are provided in the string
	valued capabilities for easy encoding of characters there.
	A  \E  (or  \e)	maps to an ESCAPE character, ^x maps to a
	control-x for any appropriate x, and the sequences  \n  \r
	\t  \b \f \s give a newline, return, tab, backspace, form-
	feed and space, respectively.  Finally, characters may  be
	given  as three octal digits after a \, and the characters
	^, \ and comma may be given as \^, \\ and \,.

	For convenience when testing entries, individual capabili-
	ties may be easily commented out by directly preceding the
	name of the capability by a period.  Thus the entry
	    33|tty33|tty|model 33 teletype,
		 cr=^M, cud1=^J, .ind=^J, bel=^G, cols#72, hc, os,
	is equivalent to the entry
	    33|tty33|tty|model 33 teletype,
		 cr=^M, cud1=^J, bel=^G, cols#72, hc, os,
	the ind capability having been 'commented out'.

	Preparing Descriptions

	We now outline how to prepare descriptions  of  terminals.
	The  most  effective way to prepare a terminal description
	is by imitating the description of a similar  terminal  in
	terminfo and  to  build up a description gradually, using
	partial descriptions with vi to check that they	are  cor-
	rect.   Be  aware  that a very unusual terminal may expose
	deficiencies in	the  ability  of  the  terminfo	file  to
	describe it or bugs in vi.  To easily test a new terminal
	description you can set the environment variable TERMINFO
	to a pathname of a file containing the description you are
	working on and the editor will look there rather than  in
	/etc/terminfo.	To  get the padding for insert line right
	(if the terminal manufacturer  did  not	document  it)	a
	severe test is to edit /etc/passwd at 9600 baud, delete 16
	or so lines from the middle of the screen,  then hit  the
	`u' key several times quickly.  If the terminal messes up,
	more padding is usually needed.	A  similar  test  can  be
	used for insert character.

	Basic capabilities

	The  number  of	columns	on each line for the terminal is
	given by the cols numeric capability.  If the terminal  is
	a  CRT, then the number of lines on the screen is given by
	the lines capability.  If the terminal wraps around to the
	beginning  of the next line when it reaches the right mar-
	gin, then it should have the am capability.  If the termi-
	nal  can clear its screen, then this is given by the clear
	string capability.  If the  terminal  overstrikes  (rather
	than  clearing a position when a character is struck over)
	then it should have the os capability.  If the terminal is
	a  printing terminal, with no soft copy unit, give it both
	hc and os.  (os applies to storage scope terminals,  such
	as  Tektronix  4010  series,  as well as hard copy and APL
	terminals.)  If there is a code to move the cursor to  the
	left  edge of the current row, give this as cr.	(Normally
	this will be carriage return, control M.)  If there  is	a
	code  to produce an audible signal (bell, beep, etc) give
	this as bel.

	If there is a code to move the cursor one position to  the
	left  (such  as backspace) that capability should be given
	as cub1. Similarly, codes to move forward, up,	and  down
	should be given as cuf1, cuu1, and cud1. These local cur-
	sor motions should not alter the text they pass over,  for
	example, you would not normally use `cuf1=\s' because the
	space would erase the character moved over.

	A very important point  here  is that  the  local  cursor
	motions	encoded in terminfo are undefined at the left and
	top edges  of  a CRT  terminal.	Programs  should  never
	attempt	to  backspace  around the left edge, unless bw is
	given, and never attempt to go up locally off the top.  In
	order  to  scroll text up, a program will go to the bottom
	of the screen and send the ind (index) string.

	To scroll text down, a program goes  to	the  top  of  the
	screen  and  sends  the	ri  (reverse  index) string.  The
	strings ind and ri are undefined when not on their respec-
	tive edges of the screen.

	The  am	capability tells whether the cursor sticks at the
	right edge of the screen when text  is  output,	but  this
	does not necessarily apply to a cuf1 from the last column.
	The only local motion which is defined from the left  edge
	is  if  bw  is  given, then a cub1 from the left edge will
	move to the right edge of the previous row.  If bw is  not
	given,  the effect is undefined. This is useful for draw-
	ing a box around the edge of the screen, for example.   If
	the  terminal has switch selectable automatic margins, the
	terminfo file usually assumes that this is  on,	i.e.  am.
	If  the	terminal  has  a command which moves to the first
	column of the next line, that command can be given as  nel
	(newline).   It	does not matter if the command clears the
	remainder of the current line, so if the terminal  has  no
	cr  and lf it may still be possible to craft a working nel
	out of one or both of them.

	These capabilities suffice to describe hardcopy and glass-
	tty terminals.  Thus the model 33 teletype is described as

	    33|tty33|tty|model 33 teletype,
		 cr=^M, cud1=^J, ind=^J, bel=^G, cols#72, hc, os,

	while the Lear Siegler ADM-3 is described as

	    adm3|3|lsi adm3,
		 cr=^M, cud1=^J, ind=^J, bel=^G,
		 am, cub1=^H, clear=^Z, lines#24, cols#80,

	Parameterized Strings

	Cursor addressing and other strings  requiring  parameters
	in  the	terminal  are described by a parameterized string
	capability, with printf(3s) like escapes %x  in	it.   For
	example, to  address  the  cursor,  the cup capability is
	given, using two parameters: the row and column to address
	to.  (Rows and columns are numbered from zero and refer to
	the physical screen visible to the user, not to any unseen
	memory.) If  the  terminal  has  memory  relative cursor
	addressing, that can be indicated by mrcup.

	The parameter mechanism uses a stack and special %  codes
	to  manipulate  it.  Typically a sequence will push one of
	the parameters onto the stack and then print  it in  some
	format.	Often more complex operations are necessary.

	The % encodings have the following meanings:

	    %%	outputs `%'
	    %d	print pop() as in printf
	    %2d	print pop() like %2d
	    %02d      print pop() like %02d
	    %3d	print pop() like %3d
	    %03d      print pop() like %03d

	    %c	print pop() like %c
	    %s	print pop() like %s

	    %p[1-9]   push ith parm
	    %P[a-z]   set variable [a-z] to pop()
	    %g[a-z]   get variable [a-z] and push it
	    %'c'      char constant c
	    %{nn}     integer constant nn

	    %+ %- %* %/ %m
		      arithmetic (%m is mod): push(pop() op pop())
	    %& %| %^  bit operations: push(pop() op pop())
	    %= %> %<  logical operations: push(pop() op pop())
	    %! %~     unary operations push(op pop())
	    %i	add 1 to first two parms (for ANSI terminals)

	    %? expr %t thenpart %e elsepart %;
		      if-then-else, %e elsepart is optional.
		      else-if's are possible ala Algol 68:
		      %? c1 %t %e c2 %t %e c3 %t %e c4 %t %e %;

	It  should  be noted that the binary operators above (e.g.
	%+, %-, %m, etc.)  all work in the usual fashion, i.e.
	  	%gx %gy %m
	yields x mod y not y mod x.

	Consider the HP2645, which, to get to row 3 and column 12,
	needs  to  be  sent  \E&a12c03Y padded for 6 milliseconds.
	Note that the order of the rows and  columns  is inverted
	here,  and that the row and column are printed as two dig-
	its.	Thus	its	cup      capability       is
	cup=\E&%p2%2dc%p1%2dY$<6>.

	The Microterm ACT-IV needs the current row and column sent
	preceded by a ^T, with the row and column  simply  encoded
	in  binary, cup=^T%p1%c%p2%c.  Terminals which use %c need
	to be able to backspace the cursor (cub1), and to move the
	cursor  up  one line on the screen (cuu1).  This is neces-
	sary because it is not always safe to transmit \n, ^D  and
	\r,  as	the  system  may  change  or  discard them.  (The
	library routines dealing with terminfo set  tty	modes  so
	that tabs are never expanded, so \t is safe to send.  This
	turns out to be essential for the Ann Arbor 4080.)

	A final example is the LSI ADM-3a, which uses row and col-
	umn   offset  by a  blank  character,  thus  cup=\E=%p1%'
	'%+%c%p2%' '%+%c.  After sending `\E=',	this  pushes  the
	first  parameter, pushes the ASCII value for a space (32),
	adds them (pushing the sum on the stack in  place  of  the
	two  previous  values) and outputs that value as a charac-
	ter.  Then the same is  done  for  the  second  parameter.
	More complex arithmetic is possible using the stack.

	If   the terminal  has	row  or	column	absolute  cursor
	addressing, these can be given as single parameter  capa-
	bilities hpa (horizontal position absolute) and vpa (ver-
	tical position absolute).   Sometimes  these  are  shorter
	than  the more general two parameter sequence (as with the
	hp2645) and can be used in preference to cup .	If  there
	are parameterized local motions (e.g. move n spaces to the
	right) these can be given as cud, cub, cuf, and cuu with a
	single  parameter  indicating  how  many spaces	to move.
	These are primarily useful if the terminal does	not  have
	cup, such as the Tektronix 4025.

	Cursor motions

	If the terminal has a fast way to home the cursor (to very
	upper left corner of screen) then this  can  be	given  as
	home;  similarly a  fast way of getting to the lower left
	hand corner can be given as ll; this may involve going  up
	with  cuu1  from the  home position, but a program should
	never do this itself (unless ll does) because it can  make
	no  assumption about the effect of moving up from the home
	position.  Note that the home  position	is  the	same  as
	addressing to (0,0): to the top left corner of the screen,
	not of memory.  (Thus, the \EH sequence	on  HP	terminals
	cannot be used for home.)

	Area clears

	If the terminal can clear from the current position to the
	end of the line, leaving the  cursor  where  it	is,  this
	should be given as el.  If the terminal can clear from the
	current position to the end  of	the  display,  then  this
	should  be given as ed.	ed is only defined from the first
	column of a line.  (Thus, it can be simulated by a request
	to  delete  a  large  number of lines, if a true ed is not
	available.)

	Insert/delete line

	If the terminal can open a new blank line before the  line
	where  the cursor is, this should be given as il1; this is
	done only from the first position of a line.   The  cursor
	must then appear on the newly blank line.  If the terminal
	can delete the line which the  cursor  is  on,  then  this
	should  be  given as dl1; this is done only from the first
	position on the line to be deleted.  Versions of il1  and
	dl1  which  take a  single parameter and insert or delete
	that many lines can be given as il and dl.  If the  termi-
	nal  has a settable scrolling region (like the vt100) the
	command to set this can be described with the csr capabil-
	ity,  which takes two parameters: the top and bottom lines
	of the scrolling region. The cursor  position  is,  alas,
	undefined after using this command.  It is possible to get
	the effect of insert or delete line using this  command	-
	the  sc and rc (save and restore cursor) commands are also
	useful.	Inserting lines at  the	top  or  bottom  of  the
	screen  can also be done using ri or ind on many terminals
	without true insert/delete line, and are often faster even
	on terminals with those features.

	If the terminal has the ability to define a window as part
	of memory, which all commands affect, it should	be  given
	as the parameterized string wind.  The four parameters are
	the starting and ending lines in memory and  the starting
	and ending columns in memory, in that order.

	If  the	terminal can retain display memory above then the
	da capability should be given; if display  memory  can  be
	retained below	then  db should be given.  These indicate
	that deleting a line  or scrolling  may	bring	non-blank
	lines  up  from	below  or that scrolling back with ri may
	bring down non-blank lines.

	Insert/delete character

	There are two basic kinds of  intelligent  terminals  with
	respect	to insert/delete character which can be described
	using terminfo.	The most common	insert/delete	character
	operations  affect only the characters on the current line
	and shift characters off the  end  of  the  line rigidly.
	Other  terminals,  such	as the Concept 100 and the Perkin
	Elmer Owl, make a distinction between  typed  and  untyped
	blanks  on  the	screen, shifting upon an insert or delete
	only to an untyped blank on the	screen	which  is  either
	eliminated,  or	expanded  to two untyped blanks.  You can
	find out which kind of terminal you have by  clearing  the
	screen  and  then typing text separated by cursor motions.
	Type abc def using local cursor  motions  (not  spaces)
	between	the  abc  and  the def.	Then position the cursor
	before the abc and put the terminal in  insert  mode.   If
	typing  characters  causes  the	rest of the line to shift
	rigidly and characters to fall off the end, then your ter-
	minal  does  not distinguish  between  blanks and untyped
	positions.  If the abc shifts over to the def  which  then
	move  together around the end of the current line and onto
	the next as you insert, you have the second type of termi-
	nal,  and  should give the capability in, which stands for
	insert null.   While  these  are two  logically	separate
	attributes  (one line vs. multi line insert mode, and spe-
	cial treatment of untyped spaces) we have seen  no  termi-
	nals whose insert mode cannot be described with the single
	attribute.

	Termcap can describe both terminals which have  an  insert
	mode, and terminals which send a simple sequence to open a
	blank position on the current  line.   Give  as	smir  the
	sequence to  get  into	insert	mode.	Give  as rmir the
	sequence to leave insert mode.	Now  give  as	ich1  any
	sequence needed	to  be	sent  just  before  sending  the
	character to be inserted.   Most terminals  with  a  true
	insert  mode  will  not	give ich1, terminals which send a
	sequence to open a screen position should  give	it  here.
	(Insert mode is usually preferable to the sequence to open
	a position on the screen if your terminal has  both.)   If
	post  insert  padding  is needed, give this as a number of
	milliseconds in ip (a string option).  Any other sequence
	which  may  need to  be	sent after an insert of a single
	character may also be given in ip.  If your terminal needs
	both to be placed into an `insert mode' and a special code
	to precede each inserted character,  then  both	smir/rmir
	and  ich1  can  be  given, and both will be used.  The ich
	capability, with one parameter, n, will repeat the effects
	of ich1 n times.

	It  is  occasionally  necessary	to  move  around while in
	insert mode to delete characters on the same line (e.g. if
	there  is  a  tab  after the insertion position).  If your
	terminal allows motion while in insert mode you	can  give
	the  capability	mir  to	speed up inserting in this case.
	Omitting mir will  affect  only	speed.	Some	terminals
	(notably Datamedia's) must not have mir because of the way
	their insert mode works.

	Finally, you can specify dch1 to delete a  single  charac-
	ter,  dch  with	one parameter, n, to delete n characters,
	and delete mode by giving smdc and rmdc to enter and  exit
	delete  mode  (any mode the terminal needs to be placed in
	for dch1 to work).

	A command to erase n characters (equivalent to  outputting
	n  blanks  without  moving the cursor) can be given as ech
	with one parameter.

	Highlighting, underlining, and visible bells

	If  your terminal  has	one  or	more  kinds  of  display
	attributes,  these  can be represented in a number of dif-
	ferent ways.  You should choose one display form as stand-
	out mode , representing a good, high contrast, easy on the
	eyes, format for highlighting  error  messages  and  other
	attention  getters.   (If you have a choice, reverse video
	plus half bright is good, or reverse  video  alone.)   The
	sequences  to  enter  and  exit standout mode are given as
	smso and rmso respectively.  If the code to change into or
	out  of	standout mode leaves one or even two blank spaces
	on the screen, as the TVI 912 and Teleray  1061	do,  then
	xmc should be given to tell how many spaces are left.

	Codes  to  begin underlining  and  end underlining can be
	given as smul and rmul respectively.  If the terminal  has
	a  code	to  underline  the current character and move the
	cursor one space to the right, such as the Microterm Mime,
	this can be given as uc.

	Other  capabilities  to	enter  various highlighting modes
	include blink (blinking) bold (bold or extra  bright)  dim
	(dim  or half  bright) invis (blanking or invisible text)
	prot (protected) rev (reverse video) sgr0  (turn off  all
	attribute  modes)  smacs (enter	alternate  character set
	mode) and  rmacs (exit	alternate  character  set  mode).
	Turning	on  any of these modes singly may or may not turn
	off other modes.

	If there is a sequence to set  arbitrary combinations  of
	modes,  this should be given as sgr (set attributes), tak-
	ing 9 parameters.  Each parameter is either 0 or 1, as the
	corresponding  attribute is  on or off.	The 9 parameters
	are, in order: standout, underline, reverse,  blink,  dim,
	bold,  invis,  protect,	alternate character set.  Not all
	modes need be supported by sgr, only those for which  cor-
	responding separate attribute commands exist.

	Terminals  with	the ``magic cookie'' glitch (xmc) deposit
	special	``cookies''  when  they	receive   mode	setting
	sequences, which affect the display algorithm, rather than
	having extra bits for  each  character.	Some  terminals,
	such  as the  HP  2621, automatically leave standout mode
	when they move to a new line or the cursor  is  addressed.
	Programs using	standout  mode	should exit standout mode
	before moving the cursor or sending a newline, unless  the
	msgr  capability,  asserting  that  it  is safe to move in
	standout mode, is present.

	If the terminal has a way of flashing the screen to  indi-
	cate  an error quietly (a bell replacement) then this can
	be given as flash; it must not move the cursor.

	If the cursor needs to be made more  visible  than  normal
	when it is not on the bottom line (to make, for example, a
	non-blinking underline into an easier  to  find	block  or
	blinking underline) give this sequence as cvvis. If there
	is a way to make the  cursor  completely invisible,  give
	that as civis.  The capability cnorm should be given which
	undoes the effects of both of these modes.

	If the terminal needs to be in a special mode when running
	a  program that uses these capbilities, the codes to enter
	and exit this mode can be given as smcup and rmcup.   This
	arises,	for example, from terminals like the Concept with
	more than one page of memory.  If the  terminal	has  only
	memory  relative cursor addressing and not screen relative
	cursor addressing, a one screen-sized window must be fixed
	into  the terminal for cursor addressing to work properly.
	This is also used for the Tektronix 4025, where smcup sets
	the command character to be the one used by terminfo.

	If your terminal correctly generates underlined characters
	(with no special codes needed) even  though  it	does  not
	overstrike,  then  you  should give the capability ul.  If
	overstrikes are erasable with a blank, then this should be
	indicated by giving eo.

	Keypad

	If the terminal has a keypad that transmits codes when the
	keys are pressed, this information can be given. Note that
	it  is  not  possible to handle terminals where the keypad
	only works in local (this applies,  for	example,  to  the
	unshifted  HP  2621  keys).   If the keypad can be set to
	transmit or not transmit, give these  codes  as	smkx  and
	rmkx.  Otherwise the keypad is assumed to always transmit.
	The codes sent by the left arrow, right arrow,  up  arrow,
	down  arrow,  and  home keys can be given as kcub1, kcuf1,
	kcuu1, kcud1, and khome respectively.  If there are  func-
	tion  keys  such as f0, f1, ..., f10, the codes they send
	can be given as kf0, kf1, ..., kf10.  If these  keys  have
	labels  other  than the default f0 through f10, the labels
	can be given as lf0, lf1, ..., lf10.  The codes	transmit-
	ted  by	certain	other	special	keys  can  be given: kbs
	(backspace), ktbc (clear all tabs), kctab (clear the  tab
	stop  in this  column), kclr (clear screen or erase key),
	kdch1 (delete character), kdl1 (delete line), krmir  (exit
	insert  mode),  kel  (clear to end of line), ked (clear to
	end of screen), kich1 (insert character	or  enter  insert
	mode),  kil1 (insert line), knp (next page), kpp (previous
	page),  kind  (scroll  forward/down),  kri  (scroll  back-
	ward/up), khts (set a tab stop in this column).

	Tabs and Initialization

	If  the terminal has hardware tabs, the command to advance
	to the next tab stop can be given as ht	(usually  control
	I).   A	``backtab''  command  which moves leftward to the
	next tab stop can be given as cbt.  By convention, if  the
	teletype modes	indicate  that tabs are being expanded by
	the computer rather than being sent to the terminal,  pro-
	grams  should  not use ht or cbt even if they are present,
	since the user may not have the tab  stops  properly  set.
	If  the terminal has hardware tabs activated by control I,
	then tabs is given, in addition to ht.  This  is normally
	used  by the  tset(1) command to determine whether to set
	the mode for hardware tab expansion.

	Other capabilities include is1, is2, and is3,  initializa-
	tion  strings for the terminal, and if, the name of a file
	containing long initialization strings.	These strings are
	expected to  set  the terminal into modes consistent with
	the rest of the terminfo description.  They  are normally
	sent  to the  terminal, by the tset(1) program, each time
	the user logs in.  They will be printed in  the	following
	order:  is1;  is2; setting tabs using tbc and hts; if; and
	finally is3.  Most  initialization  is  done  with  is2	.

	Special	terminal  modes can be set up without duplicating
	strings by putting the common sequences in is2 and special
	cases  in  is1  and  is3.  A pair of sequences that does a
	harder reset from a totally unknown state  can  be  analo-
	gously  given  as  rs1, rs2, rf, and rs3, analogous to is2
	and if.	These strings are output by the reset(1) program,
	which  is used when the terminal gets into a wedged state.
	Commands are normally placed in rs2 and rf  only if  they
	produce	annoying effects on the screen and are not neces-
	sary when logging in.  For example, the command to set the
	vt100  into  80 column mode would normally be part of is2,
	but it causes an annoying glitch of the screen and is  not
	normally needed	since the terminal is usually already in
	80 column mode.

	If there are commands to set and clear tab stops, they can
	be  given  as tbc (clear all tab stops) and hts (set a tab
	stop in the current column of every row).  If a more  com-
	plex  sequence  is  needed  to  set  the tabs than can be
	described by this, the sequence can be placed  in  is2  or
	if.

	Delays

	Certain	capabilities  control  padding	in  the	teletype
	driver.	These are primarily needed by  hard  copy  termi-
	nals,  and are used by the tset(1) program to set teletype
	modes appropriately.  Delays embedded in the  capabilities
	cr  , ind , cub1 , ff , and tab will cause the appropriate
	delay bits to be set  in  the  teletype	driver.   If  pb
	(padding baud rate) is given, these values can be ignored
	at baud rates below the value of pb .

	Miscellaneous

	If the terminal requires other than a null (zero)  charac-
	ter  as	a  pad,	then this can be given as pad.	Only the
	first character of the pad string is used.

	If the terminal has an extra ``status line'' that  is  not
	normally used by software, this fact can be indicated.  If
	the status line is viewed as an extra line below the  bot-
	tom  line,  into which	one  can cursor address normally,
	(such as the Heathkit h19's 25th line, or the 24th line of
	a  vt100 which	is set to a 23 line scrolling region) the
	capability hs should be given.  Special strings to  go  to
	the  beginning  of  the status line and to return from the
	status line can be given as tsl and fsl. (fsl must  leave
	the  cursor position in the same place it was before tsl.)
	tsl takes one parameter, which is the column number of the
	status  line  the  cursor  is  to  be moved to.	If escape
	sequences and other special commands, such  as  tab,  work
	while  in the status line, the flag eslok can be given.	A
	string which turns  off	the  status  line  (or	otherwise
	erases its contents) should be given as dsl .  If the ter-
	minal has commands to save and restore the position of the
	cursor,	give  them as sc and rc.  The status line is nor-
	mally assumed to be the same width  as  the  rest  of  the
	screen,	e.g.   cols  .	If the status line is a different
	width (possibly because the terminal  does  not	allow  an
	entire  line  to be loaded) the width, in columns, can be
	indicated with the numeric parameter wsl .

	If the terminal can move up or down half a line, this  can
	be  indicated  with  hu	(half  line up) and hd (half line
	down).  This is primarily useful for superscripts and sub-
	scripts on hardcopy terminals.  If a hardcopy terminal can
	eject to the next page (form feed), give this as ff  (usu-
	ally control L).

	If  there is a command to repeat a given character a given
	number of times (to save time transmitting a large  number
	of  identical  characters)  this can be indicated with the
	parameterized string rep.   The	first  parameter  is  the
	character  to  be repeated and the second is the number of
	times to repeat it.  Thus, tparm(repeat_char, 'x', 10)  is
	the same as `xxxxxxxxxx'.

	If  the terminal has a settable command character, such as
	the Tektronix 4025, this can be indicated with CC.  A pro-
	totype  command	character  is chosen which is used in all
	capabilities.  This character is given in the CC capabil-
	ity to identify it.  The following convention is supported
	on some UNIX systems: The environment is to  be	searched
	for  a  CC  variable, and if found, all occurrances of the
	prototype character are replaced with the character in the
	environment variable.

	Terminal descriptions  that  do	not represent a specific
	kind of known terminal, such as switch, dialup, patch, and
	network, should	include  the  gn (generic) capability so
	that programs can complain that they  don't  know  how  to
	talk  to the terminal.  (This capability does not apply to
	virtual	terminal  descriptions	for  which   the   escape
	sequences are known.)

	If  the	terminal  uses xon/xoff handshaking for flow con-
	trol, give  xon. Padding  information	should	still  be
	included so that routines can make better decisions about
	costs, but actual pad characters may not be transmitted.

	If the terminal has a ``meta key'' which acts as a  shift
	key,  setting  the  8th	bit of any character transmitted,
	this fact can be indicated with km.   Otherwise, software
	will assume that the 8th bit is parity and it will usually
	be cleared.  If strings exist to turn this  ``meta  mode''
	on and off, they can be given as smm and rmm.

	If  the terminal has more lines of memory than will fit on
	the screen at once, the number of lines of memory  can  be
	indicated with lm.  A value of 0 indicates that the number
	of lines is not fixed, but that there is still more memory
	than fits on the screen.

	If  the	terminal is one of those supported by the CB-UNIX
	virtual terminal protocol,  the	terminal  number  can  be
	given as vt.

	Media copy strings which control an auxillary printer con-
	nected to the terminal can be given as mc0: print the con-
	tents  of  the  screen, mc4: turn on the printer, and mc5:
	turn off the printer.  When the printer is  on,	all  text
	sent  to the terminal will be sent to the printer.  It is
	undefined whether the text is also displayed on the termi-
	nal screen when the printer is on.

	Strings	to  program  function keys can be given as pfkey,
	pfloc, and pfx.	Each of these strings takes  two  parame-
	ters:  the  function  key number to program (from 0 to 10)
	and the string to program it with.  Function  key  numbers
	out of this range may program undefined keys in a terminal
	dependent manner.  The difference between the capabilities
	is that pfkey causes pressing the given key to be the same
	as the user typing the  given  string,  pfloc  causes  the
	string  to  be  executed by the terminal in local, and pfx
	causes the string to be transmitted to the computer.

	Glitches and Braindamage

	Hazeltine terminals, which don't allow `~'  characters  to
	be displayed should indicate hz.

	Terminals  which ignore a linefeed immediately after an am
	wrap, such as the Concept and vt100, should indicate xenl.

	If  el  is  required  to get  rid of standout (instead of
	merely writing normal text on top of it),  xhp  should  be
	given.

	Teleray	terminals,  where  tabs turn all characters moved
	over to blanks, should  indicate xt  (destructive  tabs).
	This  glitch is also taken to mean that it is not possible
	to position the cursor on top of a ``magic cookie'',  that
	to  erase  standout  mode  it  is instead necessary to use
	delete and insert line.

	The Beehive Superbee, which is unable to correctly  trans-
	mit  the escape or control C characters, has xsb, indicat-
	ing that the f1 key is used for escape and f2 for  control
	C.   (Only  certain superbees have this problem, depending
	on the ROM.)

	Other specific  terminal problems  may	be  corrected  by
	adding more capabilities of the form xx.

	Similar Terminals

	If  there  are  two  very  similar  terminals,  one can be
	defined as being just like the other with  certain  excep-
	tions.	The  string  capability use can be given with the
	name of the  similar  terminal.	The  capabilities  given
	before  use override those in the terminal type invoked by
	use.  A capability can be cancelled with xx@ where  xx  is
	the capability.	For example, the entry

	    2621-nl, smkx@, rmkx@, use=2621,

	defines	a  2621-nl  that  does	not have the smkx or rmkx
	capabilities, and hence does not turn on the function  key
	labels  when in visual mode.  This is useful for different
	modes for a terminal, or for different  user  preferences.
	An  terminal may have as many use entries as needed.  They
	are handled in the order given in  the  description,  that
	is,  later  use's  will not overwrite capabilities defined
	earlier in the entry.

FILES
	/usr/lib/terminfo  file containing terminal descriptions
	/usr/lib/terminfo/?/*  directories  containing  compiled
		descriptions

SEE ALSO
	ex(1), curses(3), tset(1), vi(1), ul(1), more(1)

AUTHOR
	Pavel Curtis
	Zeyd M. Ben-Halim